Advanced Computer Systems Final Project
Dan Fiumara

---
All Digital Phase Locked Loop
- ADPLL allows us to synchronize periodic signals
  - Ensure accurate clock signal distribution in large scale digital circuits
  - Enable multiphase clock signal generation
  - Reduce phase noise in communication systems
  - Demodulate frequency modulated signals
  - Clock Deskewing in communication buses
  - Etc.
- ADPLL’s are essential to high performance computing systems

---
All Digital Phase Locked Loop – Feedback System
1. Measure phase noise
2. Convert phase noise measurement to a control signal
3. Adjust a digitally controlled oscillator with the control signal

---
Design Task
- Not enough time to implement a full ADPLL
- Focus on the Time to Digital Converter

---
Time to Digital Converter (TDC)
- TDC measures the time elapsed between two events
- TDC’s have tons of applications
  - ADPLL
  - Time of Flight Sensors (ToF)
  - Experimental physics measurements (measure particle speed)
  - Medical Imaging
  - Etc.

---
Time to Digital Converter
Signal Domains

---
TDC Design
- Goal: Measure the time elapsed between two pulses
- Tool: Pulse Arbiter
  - Determine which of two pulses occurs first
  - Simple Flip-Flop implementation
- Tool: Delay Element
  - Delay an input pulse by a given amount of time

---
TDC Design - Arbiter

---
TDC Design – Delay Line

---
Basic TDC Top-Level Schematic

---
Time to Digital Converter (TDC) Design Improvements
- Folded Delay Line (Ring Buffer)
- Vernier Delay Lines
- 2D Vernier Delay Lines
- Hierarchical measurement (course, fine circuits)