High Speed SerDes Transmitters
and
IC Design Automation
Dan Fiumara

---
The Need for High Speed Links
- AI/ML workloads are increasingly expensive
- Datacenters deploy thousands and thousands of GPU’s to train and run LLM’s
- We need a way to communicate die to die with very low latency to orchestrate these resources

---
Communication Interfaces
- Parallel Data Bus
  - Simple to implement
  - Very high speed
  - What is the tradeoff?
- I/O is more expensive than transistors
  - Parallel data bus spends lots of I/O for speed
  - Transistors are cheap!
  - Can we use transistors to save I/O?

---
Serial Link
- Serial Communication
  - Spend less on I/O
  - Require our infrastructure to be fast (very fast)
- We need to communicate for highly parallel workloads
- Our data is parallel at execution time
- We can Serialize the data, transmit, receive, then Deserialize

---
SerDes
- Serializing parallel data (at high speeds)
- How do we operate a circuit very fast? (clock generation)
- Fmax of a modern transistor is ~300GHz
- Becomes unstable long before 300GHz though

---
SerDes
We can use basic digital circuit building blocks to serialize our data

---
SerDes
- Peaking structures
- How can we compensate for parasitic capacitance?
  - We can utilize inductive peaking structures

---
Coplanar Waveguides
- Once our signal is very high speed (microwave region) we transport it with a waveguide
- CPW is a planar transmission line (designed to minimize power loss)

---
Results
- Shoreline Bandwidth Density = Gbps / mm
- This work achieved ~200 Gbps/mm

---
IC Design Automation
- Many aspects of this SerDes transmitter design were automated
- Generators (code defined schematics)
- Optimization loop
- This is ground breaking!

---
IC Design Automation – Surrogate Models
- Spice simulation is SLOW
- EM Simulation is SLOWER
- Iterating on designs takes too much time
- Can we approximate the simulator’s results with a deep neural network?

---
IC Design Automation – Inverse Design
- Humans design intuitive shapes
- What does the OPTIMAL shape look like?